TECHNICAL  SPECIFICATIONS:

## 1000S:

## Weight:		1.53  tonnes  (30cwt

Length			7.8  metres  (22ft

Width			2.4 metres   (8 ft

Wheels:   White Sunraisier Rims 7 x 15”

Hubs	      S/L  L/C 6 stud

## Tyres:	      235/75-15

Axles:       Suspension system: Unique crank axle

system with 3 leaf ¼ elliptic leaf travelling in upright position.  Each leaf is ½” thick

Winch System:     Winch operated crank axle for raising and lowering the unit with 12 volt electric winch with remote control

501S:

Weight:	33 panels    1.2 tonnes

45 panels    1.4 tonnes

Length:	7.8 metres

Width:		2.4 metres

Wheels:	Normally Ford rims 6 x 14”

Tyres:		185 x 14”

Hubs:		Ford hubs S/L bearings

Axle:		Suspension system:  Unique crank axle system with 3 leaf ¼ elliptic leaf spring – travelling in upright position and each leaf is 7/16” thick

Winch System:	Winch operated crank axle for raising & lowering the unit, either hand or electric is available.

17

X1 and X2 are point where centre panel locates in main unit.

Y and Z are support frame positions.