SETTING UP:   (Refer to diagram 1 & 2)

FOR  LAYOUT :  NO. 1

Detach from towing vehicle and bring vehicle to side of main unit for operation of the electric winch from the vehicle battery.  Having attached the leads to the battery, take the weight off the spring on the winch cable and remove the support pin.  Lower the spring by means of the winch standing well clear of axle & cable incase of breakage and then detach the hook and cable from the spring.  Rewind the cable to prevent tangling and possible damage.  The winch bar can now be removed from the main unit and put aside.

IMPORTANT:  When carrying out the lowering operation make sure that none of the casters are trapped under the sides of the main unit.

Remove the transport bar and block gates hanging on it and put aside.  Unfasten the securing  chain from the panels at point A1 on diagram 1.  Holding panels upright, remove chain at point A2 and swing the outer panel away from the main unit to prevent this section from falling.  Roll the complete4 sections a few yards away from the main unit towards the rear and stand so it will not fall.  Take care at this point that the outer panel of the 6 section does not start to fall.  Taking this end panel of the 6 section, walk in a curved line pulling the panels behind you.

9

GLOSSARY  OF  TERMS:

Main Unit:	The trailer section or crush including the drafting race.

Rear Sections:   These panel normally left pinned  to

3 plus 7 sections      the rear corners of the main unit  and          which form the holding yard

Front sections:   The two sets of 6 joined panels

6 sections        normally left pinned to the front corners of   the central collecting yard

4 plus 4 sections:   The 4 sets of 4 joined panels carried outside the 6 sections normally used pinned to the main unit just forward of the axle, forming the outer collection yards  see diagram No. 2

5FT Gate:    The gate normally carried across the back of the main unit

8FT Loose Gate:   The only single size gate, carried outside one of the rear sections used to make small catching pen.