Refer to layout no. 1 at this point for the standard layout.

IMPORTANT:  As previously stated, do not let the panels to form a straight line at any time or they will fall.  The inner end of the 4 section can now be pinned to the main unit at the point forward of  the axle.  This end panel should be one with the  longer hinge pins.  Joining on the other 4 section, once again walk in a curve and meet the 6 section,  the loose end of the 4 section will pin to the 6  section at this point.  Repeat this above procedure for the other 6 section and 4 section to complete  the three collection yards.  Going now to the rear half of the main unit, remove the securing chain from the panels at either C1 or C3, followed by C2 or C4.  Lift of the 8’ loose gate and pull the end panel of the rear section outwards to prevent the section falling.  Take the 8’ gate to one of the outer collecting yards an set up the mulesing  tailing pen as shown in diagram 3.

SAFETY					      7

DO’S  AND  DON’TS   in the use and care of McDougall Transportable Sheep yards.

When setting up, folding away,  using and transporting, there are several important  DO’ AND  DON’TS to be remembered.

We sincerely recommend that you read the following before using the yards for the first time.

When setting up or folding the yards:

- Do not allow panels to form a straight line as they will fall.

- When detaching or moving a section of panels, always make sure that they are spread apart and the end panels are turned away from the rest to stop the section from falling

- Keep fingers out from between the top rail of the panels when moving or folding them, or the result will at the least be very painful.

- When folding the sections onto the main unit make sure that the casters do not obstruct the folding or the total number of panels will not fit on the carrying bars.

- Do Not lean across spring when fitting transport pin as cable can break leading to injury