FOR  TRANSPORTATION:

- Make sure the transport bar is in position to keep the unit rigid.

- Make sure the winch cable has not been damaged or becomes frayed and after raising the unit take the weight of the winch onto the support pin.

- Make sure all supporting chains are securely fitted and tight.

TRANSPORTATION ON ROADS & THE LAW:

- In WA for  transporting along roadways, the minimum requirement is an orange rotation light which can be seen from all angles, and at a speed of no more than 80KPH.   For safer travel, a set of portable rear lights can be fitted.

- For transport at night, the requirements are, side clearance  and tail lights.

- OTHER STATES:   -  It is recommended that the owner checks with the relevant departments to obtain the correct laws for their respective state so infringements do not occur.

GENERAL:    SERVICE & MAINTENANCE

- Grease the crank axle from time to time through the two grease nipples provided.

- Check the hubs for grease and repack when necessary.

- Check tyres for pressure, normally 50 psi        ( 350kpa).

13

Diagram 2